## Slide 1
Chapter 1 Computer Networks
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016

## Slide 2: Internet
billions of connected computing devices (hosts, end systems)
communication links
  Twisted pair copper wire
  Coaxial cable
  Optical fiber
  Electro-magnetic
  Satellite
packet switches: routers and link-layer switches
wired
links
wireless
links
router
smartphone
PC
server
wireless
laptop
mobile network
global ISP
regional ISP
home
network
institutional
network
Notes: 2

## Slide 3: Some devices
IP picture frame
http://www.ceiva.com/
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: watch,
control cable TV remotely
Tweet-a-watt:
monitor energy use
sensorized,
bed
mattress
Internet of Things (IoT) !!

## Slide 4
Internet: “network of networks”
  Interconnected ISPs
Billions of people are using the same network. They should use standard rules. These standard rules are said protocols.
  e.g., TCP, IP, HTTP, IEEE 802.11
This class is mostly about protocols !!
Internet
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 5: Internet
infrastructure that provides services:
  Web, VoIP, email, games, e-commerce, social nets, …
provides communication interface for applications
  hooks that allow sending and receiving app programs to “connect” to Internet
  provides service options, analogous to postal service
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 6
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
TCP connection
request
protocol
-format and order of messages
-actions taken on messages

## Slide 7: Network edge
network edge:
  End systems/hosts, in which applications run
  A group of servers >> data center
access network: the network between the end system and the first router
network core:
  interconnected routers
  network of networks
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 8: Access network
home access nets (DSL, Cable)
enterprise access networks (Ethernet)
mobile access networks (3G, 4G, LTE)
What is bandwidth? Bits per second (bps)
Transmission rate typically depends on the transmission rate of the access net

## Slide 9: Home Access net: digital subscriber line (DSL)
ISP
central office
telephone
network
DSLAM
voice, data transmitted
at different frequencies over
dedicated line to central office
  The existing telephone line (twisted pair copper wire) is used for 3 purposes: phone (0-4KHz), Upstream (4-50KHz) and Downstream (50KHz-1MHz)
  This access is asymmetric as upstream and downstream rates are different
  What is in Regina? SaskTel, Access Communications !!
DSL
modem
splitter
DSL access
multiplexer

## Slide 10
ISP
data, TV transmitted at different
frequencies over shared cable
distribution network
cable
modem
splitter
…
cable headend
CMTS
cable modem
termination system
Existing cable television’s network
Coaxial cable and optical fiber - hybrid fiber coax (HFC)
Home Access net: cable

## Slide 11: Enterprise access networks: Ethernet
local area network (LAN) used in companies, universities, etc.
  Wire: End system to Ethernet switch (Link-layer switch) >> twisted pair copper wire
  Wireless: WLAN (Wi-fi): 100ft ; IEEE 802.11
Ethernet
switch
institutional mail,
web servers
institutional router
institutional link to
ISP (Internet)

## Slide 12: Mobile access net: 3G, 4G, LTE
shared wireless access network connects end system to router via base station (access point)
wide-area wireless access
  provided by telco (cellular) operator, 10’s km
  between 1 and 10 Mbps
  3G, 4G: LTE
to Internet

## Slide 13: Physical communication Link
bit: propagates between transmitter/receiver pairs
physical link: what lies between transmitter & receiver
guided media:
  signals propagate in solid media: copper, fiber, coax
unguided media:
  signals propagate freely, e.g., radio
twisted pair (TP)
two insulated copper wires
  Category 5: 100 Mbps, 1 Gbps Ethernet
  Category 6: 10Gbps

## Slide 14: Physical media: coax, fiber
coaxial cable:
two concentric copper conductors
bidirectional
broadband:
  multiple channels on cable
  HFC
fiber optic cable:
glass fiber carrying light pulses, each pulse a bit
high-speed operation:
  high-speed point-to-point transmission (e.g., 10’s-100’s Gbps transmission rate)
low error rate

## Slide 15: Physical media: radio
Electro-magnetic:
signal carried in electromagnetic spectrum
no physical wire
bidirectional
propagation environment effects:
  reflection
  obstruction by objects
  interference
radio link types:
terrestrial microwave
  e.g. up to 45 Mbps channels
LAN (e.g., WiFi)
  54 Mbps
wide-area (e.g., cellular)
  4G cellular: ~ 10 Mbps
satellite
  Kbps to 45Mbps channel
  270 msec end-end delay

## Slide 16: Network core
mesh of interconnected routers
Message + header => packet
How to send packet from one place to another? Packet-switching technique and circuit switching technique

## Slide 17: Packet Switching
Length of a packet = L bits
transmission rate = R bps
R: link transmission rate
host
1
2
two packets,
L bits each
transmit time (or transmission delay)
L
R
=
s

## Slide 18: Packet-switching: store-and-forward
store and forward: a packet cannot be transmitted before the entire packet is received
Transmit time for the first packet = 2L/R
Transmit time for the 3 packets = 4L/R
Transmit time for N communication links = NL/R
source
R bps
destination
1
2
3
L bits
per packet
R bps

## Slide 19: Packet Switching: queueing delay and packet loss
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for output link
If the link is busy, the packet is queued in buffer. Then, queueing delay
The buffer is finite. If the buffer is full and a new packet is received, then this packer cannot be stored. And, this packet is lost.

## Slide 20: Packet switching: routing table and routing protocol
routing: find the route using the forwarding tables
forwarding: move packet from router’s input to output
Routing protocols: automatically set the forwarding tables
routing algorithm
local forwarding table
header value
output link
0100
0101
0111
1001
3
2
2
1
1
2
3
0111
destination address in arriving
packet’s header

## Slide 21: Circuit switching
Resources (buffer and transmission rate) are reserved
in diagram, each link has four circuits.
  2nd circuit in top link and 1st circuit in right link are reserved
guaranteed performance
circuit segment idle if not used by call
Resources can not be shared

## Slide 22: Circuit switching: FDM versus TDM
FDM
frequency
time
TDM
frequency
time
4 users
Example:
Notes: Two simple multiple access control techniques.
Each mobile’s share of the bandwidth is divided into portions for the uplink and the downlink. Also, possibly, out of band signaling.
As we will see, used in AMPS, GSM, IS-54/136

## Slide 23: Packet switching versus circuit switching
example:
1 Mb/s link
each user:
  100 kb/s when “active”
  active 10% of time
circuit-switching:
  10 users
packet switching:
  with 35 users, probability > 10 active at same time is less than .0004 *
packet switching allows more users to use network!
N
users
1 Mbps link
…..
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 24: Internet structure: network of networks
access
net
access
net
…
…
…
…
…
…
…
…
connecting each access ISP to each other directly doesn’t scale: O(N2) connections.
access
net
access
net
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
access
net
access
net
access
net
access
net
…
Question: given millions of access ISPs, how to connect them together?

## Slide 25: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
Option: connect each access ISP to one global ISP?
Customer and provider ISPs have economic agreement.
global ISP

## Slide 26: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
But if one global ISP is viable business, there will be competitors ….
access
net

## Slide 27: Internet structure: network of networks
ISP C
ISP B
ISP A
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
access
net
But if one global ISP is viable business, there will be competitors …. which must be interconnected
IXP
peering link
Internet exchange point
IXP

## Slide 28: Internet structure: network of networks
at center: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider network (e.g., Google): private network that connects it data centers to Internet, often bypassing tier-1, regional ISPs
IXP
IXP
IXP
Tier 1 ISP
Tier 1 ISP
Google
Regional ISP
Regional ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP

## Slide 29: Packet delay
dproc: nodal processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 30
dtrans: transmission delay:
L: packet length (bits)
R: link bandwidth (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
Packet delay
dtrans and dprop
very different
propagation
nodal
processing
queueing
dnodal = dproc + dqueue + dtrans + dprop
A
B
transmission
Notes: 30

## Slide 31: Queueing delay
R: link bandwidth (bps)
L: packet length (bits)
a: average packet arrival rate
Traffic intensity = La/R
traffic intensity
= La/R
La/R ~ 0: small delay
La/R -> 1: large delay
La/R > 1: delay infinite!
average queueing delay
La/R ~ 0
La/R -> 1

## Slide 32: Packet loss
A packet can be transmitted if the link is not busy
If the link is busy, the packet is queued in buffer
If the buffer is full and a new packet is received, the packet is lost
The lost packet can be re-sent
A
B
packet being transmitted
packet arriving to
full buffer is lost
buffer
(waiting area)

## Slide 33: Throughput
throughput: rate (bps) at which bits are transferred
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
Rs bits/sec)
pipe that can carry
fluid at rate
Rc bits/sec)

## Slide 34: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 35: Throughput
10 connections (fairly) share backbone bottleneck link R bits/sec
Rs
Rs
Rs
Rc
Rc
Rc
R
per-connection end-end throughput: min(Rc,Rs,R/10)
in practice: Rc or Rs is often bottleneck

## Slide 36: Internet protocol stack (TCP/IP)
application: Determine what needs to be done and sent. This layer is a SW implementation.
  Web – Hypertext Transfer Protocol (HTTP)
  Email – Simple Mail Transfer Protocol (SMTP)
  File – File Transfer Protocol (FTP)
transport: Establish process-to-process connectivity. Error control, flow control, congestion control, application addressing (port numbers). SW implementation.
  Reliable connectivity - Transmission Control Protocol (TCP)
  Unreliable connectivity - User Datagram Protocol (UDP)
application
transport
network
link
physical

## Slide 37: Internet protocol stack (TCP/IP)
network: routing of datagrams from source to destination. Mixture of HW and SW.
  Addressing and identification – Internet Protocol (IP)
  routing protocols (OSPF, BGP)
link: data transfer between neighboring network elements. HW implementation.
  Link layer address – Media Access Control (MAC) address
  Ethernet, IEEE 802.11 (WiFi)
physical: bit level transfer. HW implementation.
application
transport
network
link
physical

## Slide 38: ISO/OSI reference model
presentation: allow applications to interpret meaning of data, e.g., encryption, compression
session: synchronization, recovery of data exchange
TCP/IP protocol stack have “missing” these layers. These services might be implemented in application layer, if needed.
application
presentation
session
transport
network
link
physical

## Slide 39: Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 40: Network security
field of network security:
  how bad guys can attack computer networks
  how we can defend networks against attacks
  how to design architectures that are immune to attacks

## Slide 41: Bad guys: put malware into hosts via Internet
malware can get in host from:
  virus: self-replicating infection by receiving/executing object (e.g., e-mail attachment)
  worm: self-replicating infection by passively receiving object that gets itself executed

## Slide 42
target
Denial of Service (DoS): attackers make resources (server, bandwidth) unavailable to legitimate traffic by overwhelming resource with bogus traffic
Bad guys: attack server, network infrastructure

## Slide 43: Bad guys can sniff packets
packet sniffing: Reads and records all packets (e.g., including passwords!)
A
B
C
src:B dest:A payload

## Slide 44: Bad guys can use fake addresses
IP spoofing: sending packet with false source address
A
B
C
src:B dest:A payload