## Slide 1
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Chapter 6 The Link Layer
and LANs

## Slide 2: Link layer
A device that runs a link layer protocol is called a node (such as host, router, switch). Every node has a Network Interface Card (NIC).
A communication channel than connects two nodes is called a links
Datagram from Network layer + Header information = frame

## Slide 3: Link layer services
Framing and link access
  Framing: datagram + header = frame
  For every NIC, there is a MAC address
reliable delivery transfer
error detection and error correction

## Slide 4: Error detection and correction
EDC= Error Detection and Correction bits
D = Data
Three approaches: Parity, checksum and Cyclic Redundancy Check (CRC)
Yes

## Slide 5: Parity checking
single bit parity:
Even parity: number of 1s including the parity bit is even
In the receiver side, if the number of 1s is not even, then there is a odd number of bits altered. How about if even number of 1s altered?
two-dimensional bit parity:
detect and correct single bit errors
0
0
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 6: Checksum
We studied this in Chapter 3 Transport Layer.

## Slide 7: Cyclic redundancy check
data = D
r+1 bits generator = G (both sender and receiver know)
choose r CRC bits, R, such that
  <D,R> is exactly divisible by G (Carry is never considered)
  receiver divides <D,R> by G. If non-zero remainder, then error is detected.

## Slide 8: CRC example
We get, <D,R> = D.2r XOR R
We need to find R such that,
D.2r XOR R = nG
=> D.2r = nG XOR R (XOR both side by R)
This gives us:
R = remainder[ ]
D.2r
G
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 9: Multiple access protocols
two types of links:
point-to-point link
  A single sender at one end of the link and a single receiver at the other end of the link
broadcast link
  Many senders and many receivers share a single link
shared wire (e.g.,
cabled Ethernet)
shared RF
(e.g., 802.11 WiFi)
shared RF
(satellite)
humans at a
cocktail party
(shared air, acoustical)

## Slide 10: Multiple access protocols
Multiple access problem: How to coordinate the access of multiple sending and receiving nodes to a shared broadcast link
If a node receives two or more packets at the same time, all packets are lost. This is called a collision.
We need Multiple Access Protocols
Three types of protocols:
  Channel partitioning protocols: TDMA, FDMA
  Random access protocols: Slotted ALOHA, ALOHA, CSMA, CSMA/CD
  Taking-turns protocols: Polling, token-passing

## Slide 11: Multiple access protocols
channel rate = R bps
Our expectation for a multiple access protocol:
  1. If there is a single node to send packets, the node can send at rate R.
  2. When M nodes want to transmit, each can send at average rate R/M
  3. There should be no master node to coordinate transmissions
  4. The protocol should be simple

## Slide 12: Time Division Multiple Access (TDMA)
Time is divided into time frames
Each time frame is divided into N time slots (if we have N nodes)
Each time slot is assigned to each node
Then, each node gets a transmission rate of R/N
If there is only one active node (with packets to send), then rest of the slots are never used
1
3
4
1
3
4
6-slot
frame
6-slot
frame

## Slide 13: Frequency Division Multiple Access (FDMA)
frequency bands
time
FDM cable
The channel with R bandwidth is divided into N smaller channels (if we have N nodes)
Each node is assigned a channel of R/N bandwidth
If there is only one active node (with packets to send), then rest of the channels are never used

## Slide 14: Slotted ALOHA
Every node can use the full channel
Time is divided into time slots
When a new packet arrives, a node transmits in the next slot
If 2 or more nodes transmit in a same slot, collision happens
If no collision happens, the node can send the next packet in next the slot
If collision happens, the node retransmits packet in each subsequent slots with probability p until success
1
1
1
1
2
3
2
2
3
3
node 1
node 2
node 3
C
C
C
S
S
S
E
E
E

## Slide 15: Slotted ALOHA: efficiency
A node is successful if this node transmits and the remaining N-1 nodes do not transmit
Probability that a node transmits = p
Probability that a node does not transmit = 1-p
Probability that N-1 nodes do not transmit = (1-p)N-1
Probability that a node is successful = p(1-p)N-1
Probability that any one of N nodes is successful = Np(1-p)N-1
find p* that maximizes = Np(1-p)N-1
for many nodes, take limit of Np*(1-p*)N-1 as N goes to infinity, gives: max efficiency = 1/e = .37=37%

## Slide 16: ALOHA
No time slots
When new packet arrives, a node transmits immediately
When a collision occurs, the node retransmits immediately with a probability p
A packet sending at t0 time is successful if no other node sends another packet in [t0-1,t0+1]
Efficiency = 18%

## Slide 17: CSMA (Carrier Sense Multiple Access)
If another node is using the channel, then do not send now.
Theoretically, there should be no collision
But, collisions can still occur due to propagation delay
When collision occurs, all packets are lost
spatial layout of nodes

## Slide 18: CSMA/CD (CSMA with Collision Detection)
If a collision is detected, then stop sending for a random amount of time.
How to detect collision?
  easy in wired LANs: measure signal strengths, compare transmitted, received signals
  difficult in wireless LANs: received signal strength overwhelmed by local transmission strength
spatial layout of nodes

## Slide 19: CSMA/CD efficiency
tprop = max prop delay between 2 nodes in LAN
ttrans = time to transmit max-size frame
efficiency goes to 1
  as tprop goes to 0
  as ttrans goes to infinity
better performance than ALOHA: and simple, cheap, decentralized!

## Slide 20: Polling protocol
There is a master node that sends a message to node 1 that node 1 can transmit a maximum number of packets; then node 2; node 3;…;node n; node1
Problems:
  polling delay: If there is a single active node, then the transmission rate will be less than R
  The entire channel fails if the master node fails
master
slaves
poll
data
data

## Slide 21: Token-passing protocol
Token is a small, special purpose packet
If a node has the token, it can transmit a maximum number of packets, and no other node can transmit
Then, it passes the token to the next node
Problems:
  If a node fails, the entire channel will fail
  Token delay
T
data
(nothing
to send)
T

## Slide 22: LAN: Addressing
  Each node in a LAN has a 48-bits MAC address.
  This address never changes.
  How to send packet from one node to another?
    Sending node includes the MAC address of destination node with the frame, and broadcasts the frame.
    All nodes receive the frame.
    In a node, if the MAC address matches, the frame is accepted;
    If the MAC address does not match, the frame is discarded.

## Slide 23: LAN: Addressing
adapter
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
(wired or
wireless)

## Slide 24: LAN: ARP
1A-2F-BB-76-09-AD
58-23-D7-FA-20-B0
0C-C4-11-6F-E3-98
71-65-F7-2B-08-53
LAN
137.196.7.23
137.196.7.78
137.196.7.14
137.196.7.88
Address Resolution Protocol (ARP) translate a IP address to a MAC, within a LAN (subnet)
Every node has an ARP table, mapping from IP address to MAC address
An ARP table is automatically generated

## Slide 25: LAN: ARP
If a node A does not have the MAC address of another node B, then the node broadcasts an ARP packet with the IP address of B.
All nodes receive the ARP packet
Only node B replies to A with its MAC address
Then, the ARP table of A is updated

## Slide 26: Sending a datagram to another subnet
datagram from A to B via R
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B

## Slide 27: Sending a datagram to another subnet
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
IP src: 111.111.111.111
IP dest: 222.222.222.222
A creates datagram with IP source A, destination B
A creates frame with R's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B

## Slide 28: Sending a datagram to another subnet
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP
Eth
Phy
The frame is sent from A to R
IP
Eth
Phy
R retrieves the datagram
MAC src: 74-29-9C-E8-FF-55
MAC dest: E6-E9-00-17-BB-4B
IP src: 111.111.111.111
IP dest: 222.222.222.222
IP src: 111.111.111.111
IP dest: 222.222.222.222

## Slide 29: Sending a datagram to another subnet
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
IP src: 111.111.111.111
IP dest: 222.222.222.222
R forwards datagram from one port to another
R creates frame with B's MAC address as destination address, frame contains A-to-B IP datagram
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 30: Sending a datagram to another subnet
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram from one port to another
R creates frame with B's MAC address as destination address, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
IP
Eth
Phy

## Slide 31: Sending a datagram to another subnet
R
1A-23-F9-CD-06-9B
222.222.222.220
111.111.111.110
E6-E9-00-17-BB-4B
CC-49-DE-D0-AB-7D
111.111.111.112
111.111.111.111
74-29-9C-E8-FF-55
A
222.222.222.222
49-BD-D2-C7-56-2A
222.222.222.221
88-B2-2F-54-1A-0F
B
R forwards datagram from one port to another
R creates frame with B's MAC address as destination address, frame contains A-to-B IP datagram
IP src: 111.111.111.111
IP dest: 222.222.222.222
MAC src: 1A-23-F9-CD-06-9B
MAC dest: 49-BD-D2-C7-56-2A
IP
Eth
Phy
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 32: Ethernet: A LAN technology
Speed: 10 Mbps – 10 Gbps
Physical topology:
  bus: All nodes are in same collision domain and can collide with each other
  star: active switch in center. Nodes do not collide with each other
switch
bus: coaxial cable
star

## Slide 33: Ethernet frame structure
8 bytes preamble : 7 bytes with pattern 10101010 and one byte with 10101011. It is used to synchronize receiver and sender clock rates, due to different transmission rate
addresses: 6 byte source and 6 bytes destination MAC addresses
type: Indicates Network Level protocols
CRC: cyclic redundancy check
dest.
address
source
address
data (payload)
CRC
preamble
type

## Slide 34: Ethernet
Some features:
connectionless: no handshaking between sending and receiving NICs
unreliable: receiving NIC doesn't send acks or nacks to sending NIC
CSMA/CD MAC protocol