## Slide 1
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Chapter 4 Network Layer:
The Data Plane

## Slide 2: Network layer
Host-to-host communication
Segment + header information = datagram
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 3: Forwarding and Routing
Two network-layer functions:
forwarding: move packets from router’s input link to appropriate output link
routing: determine which route should be followed from source to destination
  routing algorithms
  Routing protocols

## Slide 4: data plane and control plane
Data plane
determines how datagram arriving on router input port is forwarded to router output port
Implemented in hardware
Control plane
determines how datagram is routed among routers along end-end path from source host to destination host
Implemented in software
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in servers
1
2
3
0111
values in arriving
packet header

## Slide 5
control plane: traditional approach
Routing
Algorithm
Individual routing algorithm components in each and every router interact in the control plane
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 6
data
plane
control
plane
control plane: SDN approach
A distinct (typically remote) controller interacts with local control agents (CAs)
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 7: Router architecture
switch
fabric
routing
processor
input ports
output ports
data plane (hardware)
control plane (software)

## Slide 8: Input port
line
termination
link
layer
protocol
(receive)
Lookup
queueing
Lookup: forwarding table is consulted to determine which output port the datagram should be forwarded
Queuing datagrams if necessary
physical layer functions
link layer functions
switch
fabric

## Slide 9: Switch fabric
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
three types of switching fabrics
memory
memory
bus
crossbar

## Slide 10: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission, based on priority
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing

## Slide 11: IP datagram format
ver
length
32 bits
data
(variable length,
TCP or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
Number of bytes (header)
TCP or UDP
Number of bytes
(header + data)
realtime/non-realtime
for
fragmentation/
reassembly
-decremented at
each router
-max number
remaining before drop
Additional
information:
timestamp,
record route
taken, specify
list of routers
to visit.

## Slide 12: fragmentation and reassembly
Problem: MTU (maximum transmission unit) may be less than the size of datagram
Solution: Divide a datagram in many datagrams (each is called a fragment). This method is called fragmentation.
In the destination, resemble the fragments. IP header bits are used to identify and order the related fragments.
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 13: Fragmentation and reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
20 bytes
Header in every
datagram

## Slide 14: IP addressing: introduction
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces
32 bits IP addresses is associated with each interface
  Example: 233.1.3.2; 255.6.7.90, …
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1

## Slide 15: IP Addressing: Subnet
Some part of the network
  If we remove the hosts and routers, the connected interfaces form a subnet
  In a subnet, all interfaces have a common portion of IP address
  In a subnet, interfaces can physically reach each other without going through router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 16: IP Addressing: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2

## Slide 17: IP addressing: CIDR
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 18: IP addresses: how to get one?
Q: How does a host get IP address?
Manually assigned by system admin
DHCP: Dynamic Host Configuration Protocol: dynamically get address from server

## Slide 19: IP Addressing: DHCP
Why dynamic?
  reuse of addresses
  support mobile users
  lease can be renewed
DHCP overview:
  DHCP discover: host broadcasts if any DHCP server available
  DHCP offer: DHCP server responds
  DHCP request: host requests IP address
  DHCP ack: DHCP server sends ID address

## Slide 20: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 21: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 22: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 23: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7, different source port numbers

## Slide 24: NAT: network address translation
How to implement NAT?
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 25: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 26: IPv6: motivation
32-bit address space soon to be completely allocated.
additional motivation:
  header changes to facilitate QoS
  header format helps speed processing/forwarding
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation is allowed

## Slide 27: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow.”
next header: TCP or UDP
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits

## Slide 28: Transition from IPv4 to IPv6
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields

## Slide 29: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6

## Slide 30: Tunneling
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4

## Slide 31: IPv6: current status
Google: 8% of clients access services via IPv6
NIST: 1/3 of all US government domains are IPv6 capable